## Slide 1: SecurePi: A Raspberry Pi-Based Smart Security and Notification System
Members:61375070H_黃柏瑜 61375082H_林聖倫 61375017H_陳昕佑

## Slide 2: TABLE OF CONTENTS 01 04 02 05 03 06
Task Assignment
Storyline
Devices
Resource (Software), Protocols?
Challenges & Goals
Specifications
07
Gantt Chart

## Slide 3: Storyline 01

## Slide 4: Storyline
The core concept of this project is to develop an "Intelligent Surveillance System" capable of automatically detecting suspicious individuals or activities, capturing images/video, and sending alerts via SMS to administrators. In addition, various sensors (such as PIR motion sensor)will be integrated to monitor environmental conditions, ensuring real-time and accurate anomaly detection.

## Slide 5: Storyline
Key Objectives:
Automatically detect suspicious persons or intrusions and promptly notify the administrator.
Integrate multiple sensors to provide more comprehensive environmental data.
Send alarm notifications via SMS or other methods to enhance mobility and responsiveness.
Display warning information and sensor readings for convenient monitoring and operation.

## Slide 6: Task Assignment 02

## Slide 7: Task Assignment
Hardware and Sensor Integration (林聖倫) Responsible for wiring and programming the Arduino UNO and sensors, including the HC-SR501 PIR sensor, the MAX7219 8x8 LED module , etc.
Raspberry Pi and Image Processing (黃柏瑜) Responsible for setting up the Raspberry Pi 5 and Camera Module 2 NoIR, using OpenCV or a similar framework for video detection and capture.
SMS Alert and Network Functionality (陳昕佑) In charge of integrating and programming the GSM/4G module or SMS API (such as Twilio), enabling automatic SMS alerts upon anomaly detection.

## Slide 8: Devices 03

## Slide 9: Devices
Raspberry Pi 5: Serves as the core processing unit for image recognition and overall control.
Camera Module 2 NoIR: A camera module supporting night vision for surveillance, photo, and video capture.
Arduino UNO R3: Assists in sensor data collection and preprocessing, can use the nRF24L01 to communicate with the Raspberry Pi.
nRF24L01 Wireless Module: Short-range wireless transmission for data exchange between the Arduino and Raspberry Pi.
HC-SR501 PIR Sensor: Detects human infrared signals to determine if someone is passing by.
MAX7219 8x8 LED Module: Displays alert messages or status information.
GSM/4G Module (or Network Connection): Enables SMS alerts (through a SIM card or a web API service).

## Slide 10: Resource (Software), Protocols? 04

## Slide 11: Resource (Software), Protocols?
Operating System & Programming Languages: Raspberry Pi OS (Linux) + Python (or C++), Arduino IDE for Arduino development.
Image Processing: OpenCV (Python/C++) for face detection, motion detection, etc.
Messaging/Alerts: If using a hardware GSM module, communication is done via AT commands; if using a web API (e.g., Twilio), communication is done through HTTP/HTTPS or REST API calls.
Data Storage: SQLite or CSV files to store sensor data and alarm records.
Communication Protocols: nRF24L01 uses 2.4GHz RF protocol; Raspberry Pi and Arduino can exchange data via Serial or SPI; GSM modules use standard GSM AT command protocols.

## Slide 12: 05 Challenges & Goals

## Slide 13: Challenges
Hardware integration and wiring: Multiple sensors and wireless modules add complexity.(Difficulty Score:75)
Accuracy of image detection: Factors like ambient lighting and background noise must be managed. (Difficulty Score:80)
Data synchronization: Stable and reliable data exchange between Arduino and Raspberry Pi is crucial. (Difficulty Score:80)
GSM/SMS feasibility: If using SIM cards, signal strength and costs must be considered; if using a cloud API, a stable network connection is required. (Difficulty Score:85)

## Slide 14: Goals
Improve system detection accuracy and reduce false alarms.
Implement real-time SMS alerts and display warning information on-screen.
Ensure hardware and software stability for continuous operation.
Integrate sensor data and camera footage effectively for comprehensive surveillance.

## Slide 15: 06 Specifications

## Slide 16: Specifications
Detection Distance/Range: The HC-SR501 can detect motion within 7-10 meters.
Image Resolution: The Camera Module 2 NoIR supports up to 8MP stills and 1080p/30fps video recording.
Sensor Reading Frequency: The DHT11 reads temperature and humidity every 2 seconds; the HC-SR04 can emit ultrasonic pulses as needed (e.g., once per second).
Communication Speed: The nRF24L01 can reach up to 2Mbps (in theory), with actual speed depending on distance and environment.
System Response Time: Detect anomaly → Send SMS in under 5 seconds (depending on network/GSM signal).
Power Requirements: Raspberry Pi 5 requires about 5V/3A; Arduino UNO runs on 5V/USB power supply.

## Slide 17: 07 Gantt Chart

## Slide 18: Gantt Chart
INITIATIVE | OBJECTIVE | Week 1 | Week 2 | Week 3 | Week 4 | Week 5 | Week 6
Preliminary Planning & Setup | - Confirm requirements & hardware list - Install Raspberry Pi OS/Arduino IDE - Test basic sensors & camera module |  |  |  |  |  | 
Sensor & Camera Integration | - Write sensor data reading scripts - Implement OpenCV for image processing - Verify data transmission to Pi |  |  |  |  |  | 
SMS Alert Functionality | - Test GSM/4G module or API - Implement SMS via AT commands/REST API - Integrate with detection workflow |  |  |  |  |  | 
Display & Data Storage | - Test MAX7219 LED display - Integrate alert message display - Design database or CSV logging mechanism |  |  |  |  |  | 
System Integration & Testing | - Conduct end-to-end functionality tests - Adjust detection sensitivity and parameters - Validate SMS reliability |  |  |  |  |  | 
Optimization & Debugging | - Refine detection algorithms - Debug hardware wiring and code logic - Finalize user guide & documentation |  |  |  |  |  | 

## Slide 19
THANKS!